## Slide 1
Inputdlg: User Inputs:
nS (number of source optodes)
nD (number of detector optodes)
minRho (minimum S-D distance)
maxRho (maximum S-D distance) minRhoOpt (minimum optode distance)
maxGoodRho (max S–D dist for reliable SNR)
cW (coverage weighting factor)
HEAD MODEL INPUT
Make input .mshs, if user wants specific model they have to go via DOTHUB_toolbox of create .mshs
When loaded, search mshs.ADSolutionSpace. If not exist build it (need code to do this and figure out labelling)
Also want (optional) mshs.GMSurfaceMesh.node(:,4) to indicate parcels also need mshs.GMSurfaceMesh.labels
LOAD .mshs
Do PMDFs exist in associated head model folder
NO
Does head model folder with this name already exist?
Create Head Model Folder, save mshs there.
YES
NO
Calculate them, save to PMDFs.data in head mode folder
YES
Selecting a head model space
Defining an ROI
LOAD existing ROI.txt
GUI element that allows user to define GMsurface nodes that are part of the ROI through the following methods.
1) IF size(GMSurfaceMesh.node,2) ==4 && GMSurfaceMesh.labels exists;
Allow user to select from label list and add to mask. Selected label nodes in mask =1.
2) ROI drawer. Select point on surface, select radius. Add or Delete that radius from current mask
3) Select scalp point from label list 10-5, project down, draw radius. Add or Delete that radius from current mask.
Save ROI.txt in Headmodel/current/ROIs
Specify inputs
NO
Does solution space exist
Create solution space and add to .mshs
YES

## Slide 2
LOAD Head Model
LOAD ROI
Headmodel path
ROI path
ROI display
Other input entry
RUN AD (greyed until all inputs populated). Creates AD with timestamp filename. Populates inputs AND results. AND scalp pos labels
Other input entry
Dropdown options – load AD file (will populate/load inputs and outputs)
- RUN ROI builder – ROI builder should include the minOptodeSep option
Result display
Export Results as .txt (scalp pos label, array statistics)
RESULT STATS